## Slide 1
PlanteR-GB
Group 64
Winter is coming….
Zach Lerew, Travis Hodgin,
Max Schmidt, Austin Hodgin

## Slide 2
Overview
Recap
  Purpose & Goals
Current State
  Alpha Status
    Respect to defined Iterations
  System Demo
    Hardware Setup
    Initialization of System
    Advance Setup of System
  A Look at the Subsystems
Struggles
Moving Forward

## Slide 3
Recap of PlanteR-GB
Oregon Winter Seasonal Weather
  Not great…
Growing Indoors
  Expensive
  Limited System Options
  Human Schedules
Solution:
  RGB LEDs
  Scheduling
  Multiple controllers = Redundancy

## Slide 4
PlanteR-GB Current Status
Alpha
  All subsystems contain core functionality
    Many improvements or additions for more functionality
  Data flow from user to hardware
  Respect to Projected Iterations
System Demo

## Slide 5
Subsystems – Cmd Line Interface
Written in Python using Python Requests
Communicates with API Through HTTP Requests
8 Different Commands (Zone, Profile, Schedule, Demo1, Demo2, Apply Changes, Shut down)

## Slide 6
Subsystems – API and Internal State
Objectives:
  API: Provide entry point for data
  Internal State: represent system in memory
API
  RESTful http endpoint
  Routes mapped to actions
  Pistache
Internal State
  Six objects
  Four representational
  Two relational
Notes: 6

## Slide 7
Subsystems – State Composer
Objectives:
  Collect the Internal State’s currently running profile
  Gather all virtual LEDs and transpose onto the actual LEDs
Algorithm Psuedocode
  Get the current active profile from the state
  For the zones in the profile
    Get the zone state (intensity, colors, powered)
    Get the zone LEDs (virtual)
    For the LEDs in the zone
      Get the LED controller
      Get the controller’s IO port
      Get the LED’s index on the controller
      Calculate the RGB values to send
      Send the LED to the proper controller via UART serial

## Slide 8
Subsystems – LED Controller
Objective: Send data from the state composer to the LED registers
  Create LED color object
  Set RX and TX pin modes
  If Serial buffer is not empty
    Read LED index
    Read red value
    Read green value
    Read blue value
    Set RGB values for given LED index

## Slide 9
Struggles
Communication between the Arduino Nano and the Raspberry pi
  Needed to know type of input to the Nano, output from Pi
  Timing issues between State Composer and the Arduino
    RGB Colors sporadic
Serial read efficiency on Arduino Nano

## Slide 10
Moving Forward
Data Parser
Web Interface
Multiple Arduino Controllers w/ LED Strips
Mass System Testing
Bug Smashing